## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 7 Wireless and
Mobile Networks
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
4G/5G material completely updated; older 2/2.5/3G removed

## Slide 2: Wireless and Mobile Networks: context
more wireless (mobile) phone subscribers than fixed (wired) phone subscribers (10-to-1 in 2019)!
more mobile-broadband-connected devices than fixed-broadband-connected devices devices (5-1 in 2019)!
  4G/5G cellular networks now embracing Internet protocol stack, including SDN
two important (but different) challenges
  wireless: communication over wireless link
  mobility: handling the mobile user who changes point of attachment to network

## Slide 3: Chapter 7 outline
Introduction
Wireless
Wireless Links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 4: Elements of a wireless network
wired network
infrastructure

## Slide 5: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 6: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 7: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands

## Slide 8: Characteristics of selected wireless links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah

## Slide 9: Elements of a wireless network
wired network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 10: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 11: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to base station (WiFi, cellular) which connects to larger Internet
no base station, no connection to larger Internet (Bluetooth, ad hoc nets)
host may have to relay through several wireless nodes to connect to larger
Internet: mesh net
no base station, no connection to larger Internet. May have to relay to reach other a given wireless node MANET, VANET

## Slide 12: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 13: Wireless link characteristics (1)
important differences from wired link ….
  decreased signal strength: radio signal attenuates as it propagates through matter (path loss)
  interference from other sources: wireless network frequencies (e.g., 2.4 GHz) shared by many devices (e.g., WiFi, cellular, motors): interference
  multipath propagation: radio signal reflects off objects ground, arriving at destination at slightly different times
…. make communication across (even a point to point) wireless link much more “difficult”

## Slide 14: Wireless link characteristics (2)
SNR: signal-to-noise ratio
  larger SNR – easier to extract signal from noise (a “good thing”)
SNR versus BER tradeoffs
  given physical layer: increase power -> increase SNR->decrease BER
  given SNR: choose physical layer that meets BER requirement, giving highest throughput
    SNR may change with mobility: dynamically adapt physical layer (modulation technique, rate)
10
20
30
40
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4

## Slide 15: Wireless link characteristics (3)
Multiple wireless senders, receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 16: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoding: inner product: (original data) X (chipping sequence)
decoding: summed inner-product: (encoded data) X (chipping sequence)

## Slide 17: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M
… but this isn’t really useful yet!

## Slide 18: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2
… now that’s useful!

## Slide 22: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 23: IEEE 802.11 Wireless LAN
IEEE 802.11 standard | Year | Max data rate | Range | Frequency
802.11b | 1999 | 11 Mbps | 30 m | 2.4 Ghz
802.11g | 2003 | 54 Mbps | 30m | 2.4 Ghz
802.11n (WiFi 4) | 2009 | 600 | 70m | 2.4, 5 Ghz
802.11ac (WiFi 5) | 2013 | 3.47Gpbs | 70m | 5 Ghz
802.11ax (WiFi 6) | 2020 (exp.) | 14 Gbps | 70m | 2.4, 5 Ghz
802.11af | 2014 | 35 – 560 Mbps | 1 Km | unused TV bands (54-790 MHz)
802.11ah | 2017 | 347Mbps | 1 Km | 900 Mhz
all use CSMA/CA for multiple access, and have base-station and ad-hoc network versions

## Slide 24: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router

## Slide 25: 802.11: Channels, association
spectrum divided into channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
arriving host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  then may perform authentication [Chapter 8]
  then typically run DHCP to get IP address in AP’s subnet
BSS

## Slide 26: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 27: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with detected ongoing transmission by another node
802.11: no collision detection!
  difficult to sense collisions: high transmitting signal, weak received signal due to fading
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/CollisionAvoidance
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 28: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2

## Slide 29: Avoiding collisions (more)
idea: sender “reserves” channel use for data frames using small reservation packets
sender first transmits small request-to-send (RTS) packet to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions

## Slide 30: Collision Avoidance: RTS-CTS exchange
AP
A
B
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer
time

## Slide 31: 802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
Address 1: MAC address of wireless host or AP to receive this frame
Address 4: used only in ad hoc mode
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 3: MAC address of router interface to which AP is attached

## Slide 32: 802.11 frame: addressing
Internet
H1
R1
AP MAC addr
address 1
address 2
address 3
802.11 WiFi frame
R1 MAC addr
H1 MAC addr
R1 MAC addr
MAC dest addr
MAC source addr
802.3 Ethernet frame
H2 MAC addr

## Slide 33: 802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
duration of reserved
transmission time (RTS/CTS)
frame sequence # (for reliable data transfer)
2
2
4
1
1
1
1
1
1
1
1
type
from
AP
subtype
to
AP
more
frag
WEP
more
data
power
mgt
retry
rsvd
protocol
version
frame type (RTS, CTS, ACK, data)

## Slide 34: 802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
H1
BBS 2
BBS 1
switch: which AP is associated with H1?
  self-learning (Ch. 6): switch will see frame from H1 and “remember” which switch port can be used to reach H1

## Slide 35: 802.11: advanced capabilities
Rate adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 36: 802.11: advanced capabilities
power management
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobiles with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent; otherwise sleep again until next beacon frame

## Slide 37: Personal area networks: Bluetooth
less than 10 m diameter
replacement for cables (mouse, keyboard, headphones)
ad hoc: no infrastructure
2.4-2.5 GHz ISM radio band, up to 3 Mbps
master controller / clients devices:
  master polls clients, grants requests for client transmissions
radius of
coverage
C
C
C
P
P
P
P
M
C
master device
client device
parked device (inactive)
P
M

## Slide 38: Personal area networks: Bluetooth
TDM, 625 msec sec. slot
FDM: sender uses 79 frequency channels in known, pseudo-random order slot-to-slot (spread spectrum)
  other devices/equipment not in piconet only interfere in some slots
parked mode: clients can “go to sleep” (park) and later wakeup (to preserve battery)
bootstrapping: nodes self-assemble (plug and play) into piconet
radius of
coverage
C
C
C
P
P
P
P
M
C
master device
client device
parked device (inactive)
P
M

## Slide 39: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 40: 4G/5G cellular networks
the solution for wide-area mobile Internet
widespread deployment/use:
  more mobile-broadband-connected devices than fixed-broadband-connected devices devices (5-1 in 2019)!
  4G availability: 97% of time in Korea (90% in US)
transmission rates up to 100’s Mbps
technical standards: 3rd Generation Partnership Project (3GPP)
  wwww.3gpp.org
  4G: Long-Term Evolution (LTE)standard

## Slide 41: 4G/5G cellular networks
similarities to wired Internet
edge/core distinction, but both below to same carrier
global cellular network: a network of networks
widespread use of protocols we’ve studied: HTTP, DNS, TCP, UDP, IP, NAT, separation of data/control planes, SDN, Ethernet, tunneling
interconnected to wired Internet
differences from wired Internet
different wireless link layer
mobility as a 1st class service
user “identity” (via SIM card)
business model: users subscribe to a cellular provider
  strong notion of “home network” versus roaming on visited nets
  global access, with authentication infrastructure, and inter-carrier settlements

## Slide 42: Elements of 4G LTE architecture
Mobile device
(UE)
Base station
(eNode-B)
radio access
network
all-IP Enhanced Packet Core (EPC)
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
to
Internet
…
Mobile device:
smartphone, tablet, laptop, IoT, ... with 4G LTE radio
64-bit International Mobile Subscriber Identity (IMSI), stored on SIM (Subscriber Identity Module) card
LTE jargon: User Equipment (UE)

## Slide 43: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Base station:
at “edge” of carrier’s network
manages wireless radio resources, mobile devices in its coverage area (“cell”)
coordinates device authentication with other elements
similar to WiFi AP but:
  active role in user mobility
  coordinates with nearly base stations to optimize radio use
LTE jargon: eNode-B

## Slide 44: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Home Subscriber Service
stores info about mobile devices for which the HSS’s network is their “home network”
works with MME in device authentication

## Slide 45: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Serving Gateway (S-GW), PDN Gateway (P-GW)
lie on data path from mobile to/from Internet
P-GW
  gateway to mobile cellular network
  Looks like nay other internet gateway router
  provides NAT services
other routers:
  extensive use of tunneling

## Slide 46: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Mobility Management Entity
device authentication (device-to-network, network-to-device) coordinated with mobile home network HSS
mobile device management:
  device handover between cells
  tracking/paging device location
path (tunneling) setup from mobile device to P-GW

## Slide 47: LTE: data plane control plane separation
control plane
new protocols for mobility management , security, authentication (later)
MME
HSS
base station
P-GW
S-GW
base station
P-GW
S-GW
data plane
new protocols at link, physical layers
IP tunnels
extensive use of tunneling to facilitate mobility

## Slide 48: LTE data plane protocol stack: first hop
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
data
plane
P-GW
S-GW
Application
Transport
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
Link
base station
LTE link layer protocols:
Packet Data Convergence: header compression, encryption
Radio Link Control (RLC) Protocol: fragmentation/reassembly, reliable data transfer
Medium Access: requesting, use of radio transmission slots

## Slide 49: LTE data plane protocol stack: first hop
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
Application
Transport
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
Link
base station
LTE radio access network:
downstream channel: FDM, TDM within frequency channel (OFDM - orthogonal frequency division multiplexing)
  “orthogonal”: minimal interference between channels
  upstream: FDM, TDM similar to OFDM
each active mobile device allocated two or more 0.5 ms time slots over 12 frequencies
  scheduling algorithm not standardized – up to operator
  100’s Mbps per device possible

## Slide 50: LTE data plane protocol stack: packet core
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
P-GW
S-GW
base station
\
tunneling:
mobile datagram encapsulated using GPRS Tunneling Protocol (GTP), sent inside UDP datagram to S-GW
S-GW re-tunnels datagrams to P-GW
supporting mobility: only tunneling endpoints change when mobile user moves

## Slide 51: LTE data plane: associating with a BS
data
plane
P-GW
S-GW
base station
BS broadcasts primary synch signal every 5 ms on all frequencies
BSs from multiple carriers may be broadcasting synch signals
1
mobile finds a primary synch signal, then locates 2nd synch signal on this freq.
mobile then finds info broadcast by BS: channel bandwidth, configurations; BS’s cellular carrier info
mobile may get info from multiple base stations, multiple cellular networks
2
mobile selects which BS to associate with (e.g., preference for home carrier)
3
more steps still needed to authenticate, establish state, set up data plane
4
1
2
3

## Slide 52: LTE mobiles: sleep modes
data
plane
ZZZZ...
as in WiFi, Bluetooth: LTE mobile may put radio to “sleep” to conserve battery:
light sleep: after 100’s msec of inactivity
  wake up periodically (100’s msec) to check for downstream transmissions
deep sleep: after 5-10 secs of inactivity
  mobile may change cells while deep sleeping – need to re-establish association

## Slide 53: Global cellular network: a network of IP networks
…
visited mobile
carrier network
…
public Internet
and
inter-carrier IPX
…
P-GW
P-GW
home mobile
carrier network
Home
Subscriber
Server
in home network
roaming in visited network
SIM card: global identify info in home network
all IP:
carriers interconnect with each other, and public internet at exchange points
legacy 2G, 3G: not all IP, handled otherwise
home network HSS:
identify & services info, while in home network and roaming

## Slide 54: On to 5G!
goal: 10x increase in peak bitrate, 10x decrease in latency, 100x increase in traffic capacity over 4G
5G NR (new radio):
  two frequency bands: FR1 (450 MHz–6 GHz) and FR2 (24 GHz–52 GHz): millimeter wave frequencies
  not backwards-compatible with 4G
  MIMO: multiple directional antennae
millimeter wave frequencies: much higher data rates, but over shorter distances
  pico-cells: cells diameters: 10-100 m
  massive, dense deployment of new base stations required

## Slide 55: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 56: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
device moves
between networks, but
powers down
while moving
device moves within same AP in
one provider
network
device moves
among multiple
provider networks,
while maintaining
ongoing connections
device moves among APs in
one provider
network
We’re interested in these!

## Slide 57: Mobility approaches
let network (routers) handle it:
  routers advertise well-known name, address (e.g., permanent 32-bit IP address), or number (e.g., cell #) of visiting mobile node via usual routing table exchange
  Internet routing could do this already with no changes! Routing tables indicate where each mobile located via longest prefix match!

## Slide 58: Mobility approaches
let network (routers) handle it:
  routers advertise well-known name, address (e.g., permanent 32-bit IP address), or number (e.g., cell #) of visiting mobile node via usual routing table exchange
  Internet routing could do this already with no changes! Routing tables indicate where each mobile located via longest prefix match!
let end-systems handle it: functionality at the “edge”
  indirect routing: communication from correspondent to mobile goes through home network, then forwarded to remote mobile
  direct routing: correspondent gets foreign address of mobile, send directly to mobile
not
scalable
to billions of
mobiles

## Slide 59: Contacting a mobile friend:
search all phone books?
expect her to let you know where he/she is?
I wonder where Alice moved to?
Consider friend frequently changing locations, how do you find him/her?
call his/her parents?
Facebook!
The importance of having a “home”:
a definitive source of information about you
a place where people can find out where you are

## Slide 60: Home network, visited network: 4G/5G
…
visited mobile
carrier network
…
public Internet
and
inter-carrier IPX
…
P-GW
P-GW
home mobile
carrier network
Home
Subscriber
Server
in home network
roaming in visited network
SIM card: global identify info including home network
home network:
(paid) service plan with cellular provider, e.g., Verizon, Orange
home network HSS stores identify & services info
visited network:
any network other than your home network
service agreement with other networks: to provide access to visiting mobile

## Slide 61: Home network, visited network: ISP/WiFi
…
…
public Internet
…
authentication
access
server
attach
attach
authentication
access
server
ISP/WiFi: no notion of global “home”
credentials from ISP (e.g., username, password) stored on device or with user
ISPs may have national, international presence
different networks: different credentials
  some exceptions (e.g., eduroam)
  architectures exist (mobile IP) for 4G-like mobility, but not used

## Slide 62: Home network, visited network: generic
Home gateway
Home Network
  e.g.,: 128.119/16
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
Visited Network
e.g.,: 79.129/16

## Slide 63: Registration: home needs to know where you are!
Home gateway
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
end result:
visited mobility manager knows about mobile
home HSS knows location of mobile
2
visited mobility manager registers mobile’s location with home HSS
mobile associates with visited mobility manager
1
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16

## Slide 64: Mobility with indirect routing
Home gateway
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
1
correspondent uses home address as datagram destination address
home gateway receives datagram, forwards (tunnels) to remote gateway
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16
2
3
4a
4b
visited gateway router forwards to mobile
visited gateway router forwards reply to correspondent via home network (4a) or directly (4b)

## Slide 65: Mobility with indirect routing: comments
triangle routing:
  inefficient when correspondent and mobile are in same network
mobile moves among visited networks: transparent to correspondent!
  registers in new visited network
  new visited network registers with home HSS
  datagrams continue to be forwarded from home network to mobile in new network
  on-going (e.g., TCP) connections between correspondent and mobile can be maintained!

## Slide 66: Mobility with direct routing
Home gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
1
correspondent contacts home HSS, gets mobile’s visited network
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16
4
visited gateway router forwards to mobile
2
3
Correspondent addresses datagram to visited network address

## Slide 67: Mobility with direct routing: comments
overcomes triangle routing inefficiencies
non-transparent to correspondent: correspondent must get care-of-address from home agent
what if mobile changes visited network?
  can be handled, but with additional complexity

## Slide 68: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 69: Mobility in 4G networks: major mobility tasks
Mobility manager
Visited network
P-GW
Streaming server
Home
network
Internet
base station
MME
1
2
3
4
Home
Subscriber
Server
S-GW
P-GW
base station association:
covered earlier
mobile provides IMSI – identifying itself, home network
1
control-plane configuration:
MME, home HSS establish control-plane state - mobile is in visited network
2
data-plane configuration:
MME configures forwarding tunnels for mobile
visited, home network establish tunnels from home P-GW to mobile
3
mobile handover:
mobile device changes its point of attachment to visited network
4

## Slide 70: Configuring LTE control-plane elements
Mobility manager
Mobile communicates with local MME via BS control-plane channel
MME uses mobile’s IMSI info to contact mobile’s home HSS
  retrieve authentication, encryption, network service information
  home HHS knows mobile now resident in visited network
BS, mobile select parameters for BS-mobile data-plane radio channel
Visited network
P-GW
Home
network
base station
MME
2
Home
Subscriber
Server
S-GW
P-GW

## Slide 71: Configuring data-plane tunnels for mobile
Mobility manager
P-GW
Streaming server
Internet
base station
MME
Home
Subscriber
Server
S-GW
P-GW
Visited network
Home
network
S-GW to BS tunnel: when mobile changes base stations, simply change endpoint IP address of tunnel
S-GW to home P-GW tunnel: implementation of indirect routing
tunneling via GTP (GPRS tunneling protocol): mobile’s datagram to streaming server encapsulated using GTP inside UDP, inside datagram

## Slide 72: Handover between BSs in same cellular network
P-GW
S-GW
MME
source BS
1
3
2
data path before handover
data path after
handover
1
current (source) BS selects target BS, sends Handover Request message to target BS
2
target BS pre-allocates radio time slots, responds with HR ACK with info for mobile
3
source BS informs mobile of new BS
mobile can now send via new BS - handover looks complete to mobile
4
source BS stops sending datagrams to mobile, instead forwards to new BS (who forwards to mobile over radio channel)
target BS
4

## Slide 73: Handover between BSs in same cellular network
1
6
3
5
5
2
5
target BS informs MME that it is new BS for mobile
MME instructs S-GW to change tunnel endpoint to be (new) target BS
6
target BS ACKs back to source BS: handover complete, source BS can release resources
P-GW
S-GW
MME
source BS
target BS
4
7
7
mobile’s datagrams now flow through new tunnel from target BS to S-GW

## Slide 74: Mobile IP
mobile IP architecture standardized ~20 years ago [RFC 5944]
  long before ubiquitous smartphones, 4G support for Internet protocols
  did not see wide deployment/use
  perhaps WiFi for Internet, and 2G/3G phones for voice were “good enough” at the time
mobile IP architecture:
  indirect routing to node (via home network) using tunnels
  mobile IP home agent: combined roles of 4G HSS and home P-GW
  mobile IP foreign agent: combined roles of 4G MME and S-GW
  protocols for agent discovery in visited network, registration of visited location in home network via ICMP extensions

## Slide 75: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handover loss
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  bandwidth a scare resource for wireless links

## Slide 76: Chapter 7 summary
Wireless
Wireless Links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols