## Slide 1
Chapter 1 Introduction
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th Edition, Global Edition Jim Kurose, Keith Ross Pearson April 2016

## Slide 2: Chapter 1: introduction
our goal:
get “feel” and terminology
more depth, detail later in course
approach:
  use Internet as example
overview:
what’s the Internet?
what’s a protocol?
network edge; hosts, access net, physical media
network core: packet/circuit switching, Internet structure
performance: loss, delay, throughput
security
protocol layers, service models
history

## Slide 3: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history

## Slide 4: What Is the Internet?
Internet can be defined in two ways
  The basic components – i.e. the nuts and bolt
    the basic hardware and software components that make up the Internet
  The services it provide
    a networking infrastructure that provides services to distributed applications
Internet: the network of networks

## Slide 5
billions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
The ‘nuts and bolts’ view
All the pieces of the Internet run protocols that controls the sending and receiving of information
TCP/IP are two of the most important protocols in the Internet.
Notes: Transmission Control Protocol (TCP) and the Internet Protocol (IP)

## Slide 6
The ‘service’ view
These applications include
  email, Web surfing, social networks, instant messaging, Voiceover-IP (VoIP), video streaming, distributed games, peer-to-peer (P2P) file sharing, etc
  Distributed applications 🡺 involve multiple end systems exchanging data
Have Application Programming Interface (API)
  to communicate between different platforms through the Internet
Internet is a network of networks
  Interconnected ISPs
Notes: These applications include email, Web surfing, social networks, instant messaging, Voiceover-IP (VoIP), video streaming, distributed games, peer-to-peer (P2P) file sharing, television over the Internet, remote login, and much, much more.
The applications are said to be distributed applications, since they involve multiple end systems that exchange data with each other

## Slide 7: What’s the Internet: “nuts and bolts” view
billions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: 7

## Slide 8
Internet: “network of networks”
  Interconnected ISPs
protocols control sending, receiving of messages
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
What’s the Internet: “nuts and bolts” view
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 9: What’s the Internet: a service view
infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 10: “Fun” Internet-connected devices
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Smart Lock
sensorized,
bed
mattress
Tweet-a-watt:
monitor energy use

## Slide 11: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific messages sent
… specific actions taken when messages received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of messages sent and received among network entities, and actions taken on message transmission, receipt

## Slide 12
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get google.com
<html>
time
TCP connection
request
What’s a protocol?

## Slide 13
A human protocol
A computer network protocol
Notes: Introductions
specific message sent
🡪specific actions taken when message received, or other events

## Slide 14: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 14

## Slide 15: A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 16
A closer look
Network edge
Media: Wired/wireless
Network Core
Access Networks

## Slide 17
End system interaction

## Slide 18
Access networks
The network that physically connects an end system to the first router (also known as the “edge router”) on a path from the end system to any other distant end system.

## Slide 19: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 20: Access network: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  < 2.5 Mbps upstream transmission rate (typically < 1 Mbps)
  < 24 Mbps downstream transmission rate (typically < 10 Mbps)
DSL
modem
splitter
DSL access
multiplexer

## Slide 22
ISP
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream transmission rate, 2 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office
Access network: cable network

## Slide 24
Access network: cable network
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing: different channels transmitted
in different frequency bands
This is where the splitter is useful – to split between voice (phone) and data (computer)

## Slide 25
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9

## Slide 26
Access network: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (1 Gbps)
wireless access
point (54 Mbps)
wireless
devices
often combined
in single box

## Slide 28: Enterprise access networks (Ethernet)
typically used in companies, universities, etc.
  10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
  today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 30: Access networks: data center networks
high-bandwidth links (10s to 100s Gbps) connect hundreds to thousands of servers together, and to Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Courtesy: Massachusetts Green High Performance Computing Center (mghpcc.org)

## Slide 31: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  within building (100 ft.)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G: LTE
to Internet
to Internet

## Slide 32: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits (e.g. 1KB=1024 bit)
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 33: Host: sends packets of data
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
=
L (bits)
R (bits/sec)
=
Example: L=30Mbit, R=10Mbps
packet transmission delay
= L/R
= 30Mbit/10Mbps
= 3s

## Slide 34: Physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps

## Slide 35: Physical media: coax, fiber
coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  HFC
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gbps transmission rate)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 36: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WiFi)
  54 Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 10 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 37: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 37

## Slide 38: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 39
The network core

## Slide 40: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 41
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = L/R = 5 sec

## Slide 42
the source has three packets, each consisting of L bits, to send to the destination.
transmitting some of packet 1
The router employs store-and-forwarding 🡺 so must first buffer (“store”) the packet’s bits
When the router has received
all of the packet’s bits can it begin to transmit the packet onto the outbound link.
Notes: Transmit = forward

## Slide 43
Router
Time
end-end delay = 2L/R (assuming no propagation delay)
If not store-n-forward:
end-end delay = L/R (assuming no propagation delay)
end-end delay = N(L/R)
where
N = the number of links between source and destination

## Slide 44: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
if arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 45
A and B sends packets to the router
The router forwards packet to destination
When packets arrival at the router exceeds 1.5 Mbps, congestion will occur at the router as packets queue
When packets arrives and queue is full, packet will be dropped 🡺 resulting in packet loss.
Packet Switching: Queuing Delays and Packet Loss
output buffer /output queue

## Slide 46: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
destination address in arriving
packet’s header

## Slide 47: Two key network-core functions
ROUTING
FORWARDING
determines source to destination route taken by packets
  routing algorithms
Global action
move packets from router input interface to appropriate router output interface
Local Action

## Slide 48
Router R1 receives a packet
R1 checks the destination address
R1 finds the best path to destination
R1 forwards the packet (or drops it)
1
2
3
4
Packet destination: 192.168.1.1

## Slide 49: Alternative core: circuit switching
end-end resources allocated to, reserved for “call” between source & dest:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks

## Slide 50
The 4 circuit switches are interconnected by 4 links.
Each of these links has four circuits 🡺 can support 4 simultaneous connections.
Example:
If a link has a transmission rate of 1 Mbps
🡺 Each connection gets 250 kbps of dedicated transmission rate.
Each circuit ¼ of the link’s total transmission capacity for the duration of the connection.

## Slide 51: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Users will access media (e.g. cable) based on DIFFERENT frequency (Hz) allocation
Users will access media (e.g. cable) based on DIFFERENT time slot (second) allocation
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 52
With FDM, each circuit continuously gets a fraction of the bandwidth.
With TDM, each circuit gets all of the bandwidth
periodically during brief intervals of time (that is, during slots)

## Slide 53: Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
Notes: * Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 54
Not part of your syllabus – just extra knowledge

## Slide 55
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Packet switching versus circuit switching

## Slide 56
Circuit Switched – Connection-Oriented Networks

## Slide 57
Packet Switched – Connectionless Networks

## Slide 58
Circuit Switched | Packet Switched
Connection-oriented | Connectionless
Dedicated Circuit | Shared Circuit
Guaranteed level of service (Bandwidth, QoS) | Messages divided into packets
Inefficient use of Medium | Efficient use of Medium
Single path, no redundancy | Fault Tolerant, multiple possible paths

## Slide 59: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  residential, company and university ISPs
Access ISPs in turn must be interconnected.
  so that any two hosts can send packets to each other
Resulting network of networks is very complex
  evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 60: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 61: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…

## Slide 62: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to one global transit ISP?
Customer and provider ISPs have economic agreement.
global ISP

## Slide 63: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
access
net

## Slide 64: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
IXP

## Slide 65: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
… and regional networks may arise to connect access nets to ISPs

## Slide 66: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
IXP
IXP
access
net
access
net
access
net
regional net
Content provider network
… and content provider networks (e.g., Google, Microsoft, Akamai) may run their own network, to bring services, content close to end users

## Slide 67: Internet structure: network of networks
at center: small number of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g., Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
  Example ISP list in Malaysia: List , Service Offer , Service Cost
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP

## Slide 68: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence

## Slide 69: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 69

## Slide 70: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 71: How do loss and delay occur?
packets queuing (delay)
packet being transmitted (delay)
Queue is full, packet dropped (loss)

## Slide 72
The nodal delay at router A
A packet goes through a series of delays at each node along the path
dproc
dtrans
dqueue
dprop
Total nodal delay = dnodal = dproc + dqueue + dtrans + dprop
Notes: Total nodal delay = nodal processing delay + queuing delay + transmission Delay + propagation delay

## Slide 73: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 74
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
Four sources of packet delay
dtrans and dprop
very different
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Notes: 74
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
* Check out the Java applet for an interactive animation on trans vs. prop delay

## Slide 75: Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car ~ bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 76: Caravan analogy (more)
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one (1) min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 77: Queueing delay (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1

## Slide 78: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute/tracert program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 79
the destination system
The IP address of the hop
Round Trip Time (RTT):
The time it takes for a packet to get to a hop and back, displayed in milliseconds (ms).
🡺 By default, tracert sends 3 packets to each hop, so the output lists three roundtrip times per hop.
Hop number: The specific hop number in the path from the sender to the destination.

## Slide 80: “Real” Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org

## Slide 81: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
Notes: * Check out the Java applet for an interactive animation on queuing and loss

## Slide 82: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
Rs bits/sec
RC bits/sec

## Slide 83: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 84
If Rs < Rc
  Flow from Server to Client not interrupted
  Throughput = Rs
If Rs > Rc
  Flow from Server to Client is interrupted, queue may form
  Throughput = Rc
Throughput = min{Rc, Rs},
🡺 the transmission rate of the bottleneck link
Notes: Tip:
In bottleneck link,
Throughput = the rate of the link on the end-to-end path that constrains end-to-end throughput 🡺 whichever is smaller

## Slide 85
Throughput for a file transfer from server to client
Throughput = min{R1, R2,..., RN},
Throughput = min{Rc, Rs},

## Slide 86: Example A
The time it takes to transfer a large file of F bits from server to client as F/min{Rs, Rc}
Say, you are downloading a file of F = 32 million bits, the server has a transmission rate of Rs = 2 Mbps, and you have an access link of Rc = 1 Mbps.
The time needed to transfer the file is
Transfer time = (32 x 106) bits/1Mbps
= 32 seconds
Notes: Of course, these expressions for throughput and transfer time are
only approximations, as they do not account for store-and-forward and processing delays as well as protocol issues.

## Slide 87: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
Notes: * Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 88
End-to-end throughput: Internet scenario
Example B:
If Rs = 2Mbps, Rc = 1Mbps, R = 5Mbps, what is the throughput?
Answer:
Because R is shared, what is available for each link is (5Mbps/10) = 500kbps
Throughput = 500kbps

## Slide 89
Suppose Host A wants to send a large file to Host B. The path from Host A to Host B has 3-links, of rate R1=150kbps, R2=2Mbps, and R3=1Mbps.
i) Assuming no other traffic in the network, what is the throughput for the file transfer? Justify your answer. [2 mark]
Throughput = min(R)=150 kbps
ii) Suppose the file is 4 million bytes. Roughly, how long will it take to transfer the file to Host B? [5 marks]
Time transfer=4*106*8/(150*103)=213.3 seconds
Calculation: Example 1

## Slide 90
Host A wants to send a 30-Mbit MP3 file to host B. All the links in the path between source and destination have a transmission rate of 10Mbps. Assume that the propagation speed is 2*108 meters/sec, and the distance between source and destination is 10km. Initially suppose there is only one link between the source and the destination. Also suppose that the entire MP3 file is sent as one packet (Ignore processing delay and queuing delay). Show your workings.
i) Calculate the transmission delay?
transmission delay = L/R = 30M/10Mbps = 3s
ii) What will be the end-to-end delay?
Dprop = d/s = 10000/2*108 = 0.00005s
Dtotal = 3+0.00005 = 3. 00005s
iii) How many bits will the source have transmitted when the first bit of the MP3 file arrives at the destination?
R* Dprop = 10Mbps*0.00005s=500bit
Calculation: Example 2

## Slide 91: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 91

## Slide 92: Protocol “layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 93: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 94: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 95: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 96
ISO/OSI reference model
Open System Interconnection (OSI) model defines a generic networking framework to implement protocols in seven (7) layers
Generic OSI Model |  |  | 
 | Data unit | Layer | Function
Host layers | Data | 7. Application | Network process to application
 |  | 6. Presentation | allow applications to interpret meaning of data, e.g. data representation, encryption and decryption, convert machine dependent data to machine independent data
 |  | 5. Session | Interhost communication, managing sessions between applications, synchronization, data recovery
 | Segments | 4. Transport | Reliable delivery of packets between points on a network.
Media layers | Packet/Datagram | 3. Network | Addressing, routing and (not necessarily reliable) delivery of datagrams between points on a network.
 | Bit/Frame | 2. Data link | A reliable direct point-to-point data connection.
 | Bit | 1. Physical | A (not necessarily reliable) direct point-to-point data connection.

## Slide 97: OSI Model: AN Analogy: Application Layer - Source Host
After riding your new bicycle a few times in Tokyo, you decide that you want to give it to a friend who studies in UTM, JB.

## Slide 98: Presentation & Session Layer - Source Host
PRESENTATION:
Make sure you have the proper directions to disassemble and reassemble the bicycle.
SESSION:
Call your friend and make sure you have his correct address.

## Slide 99: OSI Model Analogy :Transport Layer - Source Host
Disassemble the bicycle and put different pieces in different boxes. The boxes are labeled
“1 of 3”, “2 of 3”, and “3 of 3”.

## Slide 100: OSI Model Analogy: Network Layer - Source Host
Put your friend's complete mailing address (and yours) on each box. Since the packages are too big for your mailbox (and since you don’t have enough stamps) you determine that you need to go to the post office.

## Slide 101: OSI Model Analogy: Data Link Layer – Source Host
Tokyo post office takes possession of the boxes.

## Slide 102: OSI Model Analogy: Physical Layer - Media
The boxes are flown from Tokyo to JB

## Slide 103: OSI Model Analogy : Data Link Layer - Destination
UTM post office receives your boxes.

## Slide 104: OSI Model Analogy: Network Layer - Destination
Upon examining the destination address, UTM post office determines that your boxes should be delivered to the written home address.

## Slide 105: OSI Model Analogy : Transport Layer - Destination
Your friend calls you and tells you he got all 3 boxes and he is having another friend named FARIS reassemble the bicycle.

## Slide 106: Session & Presentation Layer - Destination
SESSION:
Your friend hangs up because he is done talking to you.
PRESENTATION:
FARIS is finished and “presents” the bicycle to your friend. Another way to say it is that your friend is finally getting his “present”.

## Slide 107: OSI Model Analogy : Application Layer - Destination
Your friend enjoys riding his new bicycle in UTM.

## Slide 108: Internet protocol stack (TCP/IP model)
TCP/IP was developed by Advanced Research Projects Agency (ARPA) to build a nationwide packet data network in 1960s. It was first used in UNIX-based computers in universities and government installations. Today, it is the main protocol used in all Internet operations.
Notes: 1960s – TCPIP
1970s – OSI

## Slide 109: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 110: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 111: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 112
Encapsulation

## Slide 113: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 113

## Slide 114: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” ☺
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 115: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam, DDoS attacks

## Slide 116: Bad guys: put malware into hosts via Internet
Malware = malicious software
  Examples: Worm, Virus, Trojans, spyware, botnet, etc.
Malware can be
  Self-replicating 🡺 once it infects one host, from that host it seeks entry into other hosts over the Internet, and just keep going
  User activated (click on an email attachment) or
  Program activated (a vulnerable app that activates malware)
  Recruiting your device to be part of a botnet, to be use for any purpose later

## Slide 117
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts
Bad guys: attack server, network infrastructure

## Slide 118
Denial of Service (DoS):

## Slide 119: Bad guys can sniff packets
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 120
Packet “sniffing”:

## Slide 121: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload

## Slide 122
IP spoofing:

## Slide 123: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 123

## Slide 124: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 125
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets
Internet history

## Slide 126
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: CSnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
Internet history

## Slide 127
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps
Internet history

## Slide 128
2005-present
~5B devices attached to Internet (2016)
  smartphones and tablets
aggressive deployment of broadband access
increasing ubiquity of high-speed wireless access
emergence of online social networks:
  Facebook: ~ one billion users
service providers (Google, Microsoft) create their own networks
  bypass Internet, providing “instantaneous” access to search, video content, email, etc.
e-commerce, universities, enterprises running their services in “cloud” (e.g., Amazon EC2)
Internet history

## Slide 129: Introduction: summary
covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
you now have:
context, overview, “feel” of networking
more depth, detail to follow!

## Slide 130
Chapter 1 Additional Slides

## Slide 131
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received